## Slide 1: Design and FPGA Implementation of a 100-Neuron Spiking Neural Network Functionality

## Slide 2
COMPARISON
Feature | Single Neuron | Proposed System (3-100-2 Spiking)
Network Scale | 1 Neuron total | 102 Neurons total (100 Hidden + 2 Output)
Hardware Style | Basic parallel block | Time-Multiplexed FSM Pipeline (Advanced)
Output Type | Single static value / state | Spike Firing Frequency (Population Coding)
4-Bit Multiplier Use | Used only 3 times per cycle | Reused 300 times via the memory loop
Display Meaning | Shows a single raw result | Shows total system spikes (00 to 99)
Memory Footprint | Static registers; no ROM/RAM required | Embedded ROM Array required to store 300 independent weight parameters (100 X 3 )
Application Realism | Limited to basic logic gates (AND/OR); fails on non-linear data | True Edge-AI Pattern Classifier; capable of complex tasks like image edge detection

## Slide 3
Spike 1
Spike 2
Spike 3
…….
Spike 100
Input Layer
Hidden Layer
Output Layer
1
3
2
100
…..
S > Threshold

## Slide 4
SYSTEM ARCHITECTURE
Input Layer ↓ Hidden Layer (100 Neurons) ↓ Output Layer
Inputs: Input 1 (x0) , Input 2 (x1) , Input 3 (x2)
Outputs: output_neuron_0, output_neuron_1
Hidden Layer (100 Neurons): Each neuron computes:
Where:
are neuron weights.
is the bias.
is the neuron activation value.

## Slide 6
ARCHITECTURAL OVERVIEW
The network receives three input signals: (x_0), (x_1), and (x_2).
Each input is connected to all 100 hidden neurons, and every hidden neuron has its own set of weights and bias.
Every hidden neuron computes a weighted sum: + + Bias
The neuron generates a spike based on a threshold condition: spike generated 1, if S > Threshold 0, if S < Threshold
The spikes from all 100 hidden neurons are accumulated to obtain the total spike count:
Spike_Count =
The total spike activity is used to generate the two output neurons (output_neuron_0 and output_neuron_1) and is simultaneously displayed on the Basys 3 seven-segment display.

## Slide 7
FPGA IMPLEMENTATION

## Slide 8
POWER ANALYSIS
Ultra-Low Consumption: The system draws only 94 mW in total, which is less than a tenth of a watt.
I/O Dominance: 88% of the active (dynamic) power is spent driving the physical pins for your 7-segment display and LEDs, while the internal neuron math takes almost nothing.
Thermal Performance: The chip runs at 25.5°C (virtually room temperature), meaning it will never overheat.

## Slide 9
UTILIZATION ANALYSIS
Tiny Resource Footprint: The entire project uses just 162 LUTs (logic gates) and 53 Registers (storage cells).
Time-Multiplexing Proof: Because your FSM loops a single physical neuron block 100 times instead of building 100 separate hardware neurons, the design takes up less than 1% of the available chip space.

## Slide 10
TIMING ANALYSIS
Perfect Timing: There are zero failures or data corruption risks (TNS = 0.000 ns).
High-Speed Margin: Worst Negative Slack is +6.408 ns. Since the clock allows 10 ns for calculations, your circuits finish their math in just 3.592 ns—meaning your network runs nearly 3 times faster than required.

## Slide 11
RESULT ANALYSIS
Given Input: x0 = 4, x1 = 4, x2 = 4
These three input values are applied to all 100 hidden neurons.
Hidden Layer Processing
Each hidden neuron computes:
Since every neuron has different weights and bias values:
Neuron 0 → produces one activation value
Neuron 1 → produces another activation value
...
Neuron 99 → produces another activation value
Although the inputs are the same, the outputs of the neurons differ because their weights are different.

## Slide 12
RESULT ANALYSIS
Spike Generation
Each neuron compares its activation value with the threshold:
If activation > Threshold Spike = 1 Else Spike = 0
As a result: 43 neurons generated spikes 57 neurons remained inactive
Population Spike Count
The spikes from all 100 neurons are accumulated: Total Spike Count = Number of firing neurons = 43
Therefore: Seven-Segment Display = 43

## Slide 13
THANK YOU